## Slide 1: A Presentation on M I R A
Presented by:-
John Subba
Sudeep Khadka
Kaustuv Baral

## Slide 2: Contents
Introduction
Objective
Literature Review
Features
Block Diagram
Hardware Requirements
Software Requirements
Algorithms
Pre-Configuration Requirements
Circuit Diagram
Gantt Chart
Conclusion
References

## Slide 3: Introduction
M-I-R-A stands for Micro-controller Integration by Radio-Frequency in Automation system.
8051 micro-controller will act as the processing component of the system.
It uses DTMF(Dual Tone Multi-Frequency) as input for controlling the appliances attached to the output of 8051.

## Slide 4: Objective
To control electrical home appliances using cell-phones.
To detect and notify objects in the entrance passage(door).

## Slide 5: Literature Review
Research on 8051 micro-controller based projects on websites such as nevonprojects, circuitstoday, lastminuteengineers etc.
DTMF technology(Dual Tone Multi- Frequency).
Home Automation Systems.

## Slide 6: Features
Long Range of control (limited by the existence of cellular carrier cell towers).
Give command directly by calling to the sim number.
Receive Alert messages through the SMS.

## Slide 7: Block Diagram
LCD
8051/52
MCU
SIM800L
LIGHTS
FAN
Relay
driver
IR sensor
Phone
AIR
COOLER
WATER
HEATER
RECORD
PLAYER

## Slide 8: Hardware Requirements
8051/52 Micro-controller
SIM800L GSM Module
PCB/Breadboard and connecting wires
Infrared Sensor
LCD Display(16x2)
ULN2003A Relay Driver
3-4pcs (5v relay with plug and socket for 220v)

## Slide 9: Software Requirements
Keil Compiler
Proteus 8 for simulation
Micro-Controller programming language – C/Embedded C

## Slide 10: DTMF Technology
Used in touch tone phones, best known for sound made when pressing a number key.
It signals the phone company that you want to make call and send a command to the switch by sending 2 tones(1 high and 1 low) for each number pressed.

## Slide 11: Frequency Chart
F2 F1 | 1209 Hz | 1336 Hz | 1477 Hz
697Hz | 1 | 2 | 3
770 Hz | 4 | 5 | 6
852 Hz | 7 | 8 | 9
941 Hz | * | 0 | #

## Slide 12: Algorithm
Step 1: Start.
Step 2: Supply the power to the system.
Step 3: Configure phone-number for DTMF based control.
Step 4: Wait for call in sim module and activate as per the desired extension number for start/stop various loads.
Step 5: Display in LCD relevant messages.
Step 6: Monitor for IR Sensor input.
if input notify user via SMS, else goto step 4.
Step 7: Stop.

## Slide 13: Pre-Configuration Requirements
Automatically pick any incoming call after 1 ring.
Enable DTMF decoder in SIM800 (AT command data sheet for parameters).
Listen for incoming DTMF values on the serial connection.
Programmed dial pad numbers:
  1 for turning ON relay 1 and 2 for turning OFF relay 1.
  3 for turning ON relay 2 and 4 for turning OFF relay 2.
  5 for turning ON relay 3 and 6 for turning OFF relay 3. and so on...

## Slide 14: Circuit Diagram

## Slide 15: Gantt Chart
Task | January | February | March |  | April |  | May | June
Requirement gathering & analysis |  |  |  |  |  |  |  | 
Hardware selection & configuration |  |  |  |  |  |  |  | 
Database design and implementation |  |  |  |  |  |  |  | 
UID & Java Prrogramming |  |  |  |  |  |  |  | 
Testing and debugging |  |  |  |  |  |  |  | 
Documentation |  |  |  |  |  |  |  | 

## Slide 16: Conclusion
M-I-R-A is a system aimed to utilize the cell phones to control it with minimal or no physical human effort to On/Off the appliance switch as well as monitor surrounding environment using various sensors.

## Slide 17: Reference
Muhammad Ali Mazidi et al.(Oct 01, 2022). The 8051 Microcontroller and Embedded Systems.
Nevon Projects (Oct 10, 2022). Digitally controlled home automation projects. https://nevonprojects.com/digitally-controlled-home-automation-project/
Last Minute Engineers (Oct 20,2022). Send Receive SMS & Call with SIM800L GSM Module & Arduino. https://lastminuteengineers.com/sim800l-gsm-module-arduino-tutorial/

## Slide 18: Any Questions/Queries?
THANK YOU!